A new concept in satellite navigation
U. Kostić, M. Horvat, A. Gomboc
University of Ljubljana, Faculty of Mathematics and Physics

---
GNSS today
Earth tracking stations allow us to determine positions of the satellites.
When a user of navigation receives a signal from the satellites, he can use positions of the satellites to determine his coordinates on Earth.
The accuracy of acquired coordinates depends on the accuracy of satellites' positions.
receiver
satellite tracking
from Earth
position of satellites
position of the receiver

---
Relativistic GNSS
communication link between satellites
Because tracking stations are under influence of tectonic motion and tides, the positions can be determined only with limited accuracy.
If satellites communicated between one another, tracking stations would no longer be required, which would help us avoid some sources of positioning inaccuracy.
satellite tracking from Earth is no longer required
satellite tracking
from Earth
position of satellites
receiver
position of the receiver

---
Relativistic GNSS
communication link between satellites
reduction of
inter-satellite
communication data
In this case, the theory of general relativity allows us to determine satellites' positions using inter-satellite communication.
An Autonomous Basis of Coordinates (ABC) can be established in this way, to form a foundation for an RGNSS – Relativistic Global Navigation System.
Positions acquired within RGNSS are determined with great accuracy, since no tracking stations on Earth are used in this process.
ABC – Autonomous Basis of Coordinates
Univerza v Ljubljani, ESA Advanced Concepts Team (2009-2014)
position of satellites
position of the receiver
receiver

---
Advantages of RGNSS
routine measurements of tectonic plates motion
Because such a system is independent of Earth, it is possible to routinely measure the motion of the tectonic plates, just by arranging a number of receivers across the Earth's surface.
(Zuheir Altamimi, ITRF)

---
measurements of space-time curvature around Earth
Satellites, that make the RGNSS, actually map the space-time around Earth.
Because the ABC, and with it also the RGNSS, are based on the theory of general relativity, it is possible with this system to measure the space-time curvature arising from Earth and nearby celestial objects, such as the Moon, the Sun, Jupiter, and Venus.

---
measurements of the shape of Earth
Due to great accuracy of and RGNSS, it is possible to use it for measuring the tiniest differences of the space-time curvature arising from non-spherical shape of Earth.
In this way, an RGNSS can contribute a share to the existing methods of measuring the shape of Earth.
(GEMOC ARC National Key Centre, Sydney)
(GFZ, Potsdam)

---
Robustness
Great accuracy
Possibility to use the system as a clock with long term stability
Tracking stations on Earth are no longer required
Useful in science
geophysics
relativistic gravitation
Last, but not least, since the core of an RGNSS lies in the very well known motion of the satellites, such a system can be used as a clock with long term stability.